## Slide 1: COMP 261 Lecture 14
3D Graphics 2 of 2

## Slide 2: Doing better than 3x3?
Translation, scaling, rotation are different.
Awkward to combine them.
Use homogeneous coordinates :
  Convert 3D vectors to 4D vectors
  use 1 for the value in the 4th dimension
  express transformations by a 4 x 4 matrix.
Lets us combine a sequence of transformations into a single transformation
See more here: http://www.essentialmath.com/AffineXforms.pps

## Slide 3: Affine transformations: 4D
Translation:
Scale:
Rotation:
x
y
z
1
1 | 0 | 0 | ∆x
0 | 1 | 0 | ∆y
0 | 0 | 1 | ∆z
0 | 0 | 0 | 1
⇒
x ∙ sx
y ∙ sy
z ∙ sz
1
x+∆x
y+∆y
z+∆z
1
⇒
1 | 0 | 0 | 0
0 | cosθ | -sinθ | 0
0 | sinθ | cosθ | 0
0 | 0 | 0 | 1
x
y
z
1
⇒
1x + 0y + 0z
0x + cosθy – sinθz
0x + sinθy + cosθz
1
sx | 0 | 0 | 0
0 | sy | 0 | 0
0 | 0 | sz | 0
0 | 0 | 0 | 1
x
y
z
1

## Slide 4: Transformations
Apply transformation
  input: point (x, y, z, 1)
  transform T (4x4 array)
  initialise newpoint to (0,0,0,1)
  for row ← 0 to 3
    for col ← 0 to 3
      newpoint[row] += T[row, col] * point[col]
  Consistent pattern for all transformations.
To transform polygon,
  apply transform to each vertex.

## Slide 5: Combining transformations:
Translation followed by Rotation:
Matrix multiplication is associative:
x
y
z
1
1 | 0 | 0 | ∆x
0 | 1 | 0 | ∆y
0 | 0 | 1 | ∆z
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | sinθ | -cosθ | 0
0 | cosθ | sinθ | 0
0 | 0 | 0 | 1
1 | 0 | 0 | ∆x
0 | sinθ | -cosθ | sinθ∆y-cosθ∆z
0 | cosθ | sinθ | cosθ∆y+sinθ∆z
0 | 0 | 0 | 1
x
y
z
1

## Slide 6: Rendering
Viewing perspective:
Assume viewer looks along z-axis
Rotate and translate object to make this the desired view
Remove polygons facing away from viewer

## Slide 7: Remove hidden polygons
Compute normal to surface:
  (vector perpendicular to surface, pointing out of the face)
facing away from viewer if z-component of normal is +ve
  normal = edge1  edge2 (cross product of the vectors)
  n = (nx, ny, nz)
  = (aybz – azby , azbx – axbz , axby – aybx )
Remove if
    axby > aybx
  or
  (x2-x1)(y3-y2) > (y2-y1)(x3-x2)
a = (ax, ay, az) =
(x2-x1, y2-y1, z2-z1)
b = (bx, by, bz) =
(x3-x2, y3-y2, z3-z2 )

## Slide 8: Simple Z-buffer Rendering Pipeline
  input: set of polygons
  viewing direction
  direction of light source(s)
  size of window.
  output: an image
  Actions
    rotate polygons and light source so viewing along z axis
    translate & scale to fit window / clip polygons out of view
    remove any polygons facing away from viewer (normalz> 0)
    for each polygon
      compute shading
      work out which image pixels it will affect
      for each pixel write shading and depth to z-buffer (retains only the shading of the closest surface)
    convert z-buffer to image
z
x
z
y
x
y

## Slide 9: Illumination
Light reflected from a surface depends on
  light sources
  reflectivity
  matte vs shiny → diffuse or specular reflection
  color, texture, pattern, … (variation in reflectivity)
Simple option:
  assume matte, uniform reflectance for red, green, blue:
    (Rr, Rg, Rb)
  assume some ambient light
    light ← reflectance  ambient light level
  diffuse reflection depends on light source direction:
    light ← reflectance  light source  cos(angle of incidence)
    cos(θ) = normal ∙ lightdirection
    (if both unit vectors: length 1)
θ
light source
dot product

## Slide 10: Computing Illumination
  Matte or Diffuse material, “Lambert law”:
  Amount of light reflected is proportional to the cosine of the angle between the incoming light direction, and the surface normal
  We’re given the light direction
  Need to calculate the surface normal

## Slide 11: Unit Normal to surface
Normal =
  n = (nx, ny, nz)
  = (aybz – azby , azbx – axbz , axby – aybx )
  where
  ax = (x2-x1) ay = (y2-y1) az = (z2-z1)
  bx = (x3-x2) ay = (y3-y2) bz = (z3-z2)
Unit normal (perpendicular vector of length 1) =
  where
a = (ax, ay, az) =
(x2-x1, y2-y1, z2-z1)
b = (bx, by, bz) =
(x3-x2, y3-y2, z3-z2 )
Cross product

## Slide 12: Computing Illumination
  input: n = (nx, ny, nz ) surface normal unit vector
  d = (dx, dy, dz ) light direction unit vector
  (ar, ag, ab) ambient light level
  (Rr, Rg, Rb) reflectance in each colour
  (Ir, Ig, Ib) intensity/colour of incident light
  output: (Or, Og, Ob)
  actions
    costh ← n ∙ d [ = (nx dx + ny dy + nz dz ) ]
    for c in red, green, blue:
      Oc ← (ac + Ic  costh)  Rc

## Slide 13: Further reading…for geeks!
Shading languages:
  Renderman shading language
  GLSL
  Adobe Pixel Bender
  Playstation Shader Language
  Etc…

## Slide 14: Further reading…for geeks!
Shading languages:
  Syntax similar to C or Java
  Built in variables like N (= normal), I (= eye)
  Special operations like . (= dot product)

## Slide 15: Shading
Light reflected from a polygon:
  could be uniform (if assume each polygon is a flat, uniform surface)
    ⇒ compute once for whole polygon
  could vary across surface (if polygons approximate a curved surface)
  Can interpolate from the vertices:
    use "vertex normals" (average of surfaces at vertex)
    either interpolate shading from vertices
    or interpolate normals from vertices and compute shading
What about shadows and reflected light from other sources
  ray tracing!! expensive, we will ignore it
